## Slide 1: UNIT 1
Introduction to computer systems
Overview of Organization and Architecture

## Slide 2: COMPUTER ARCHITECTURE AND ORGANIZATION
Computer architecture refers to those attributes that have a direct impact on the logical execution of a program.
Examples of architectural attributes include the
instruction set,
the number of bits used to represent various data types (e.g., numbers, characters),
I/O mechanisms, and
techniques for addressing memory.

## Slide 3: Contd…
Computer organization refers to the operational units and their interconnections that realize the architectural specifications.
Organizational attributes include those
hardware details transparent to the programmer, such as control signals;
interfaces between the computer and peripherals; and
the memory technology used.

## Slide 4: COMPUTER SYSTEM
A computer is a complex system; contemporary computers contain millions of elementary electronic components.
A hierarchical system is a set of interrelated subsystems, each of the latter, in turn, hierarchical in structure until we reach some lowest level of elementary subsystem.

## Slide 5
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit Intel processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit Intel processor , referred to as IA32
  Added “flat addressing”, capable of running Unix
Pentium 4E 2004 125M 2800-3800
  First 64-bit Intel x86 processor, referred to as x86-64
Core 2 2006 291M 1060-3333
  First multi-core Intel processor
Core i7 2008 731M 1600-4400
  Four cores (our shark machines)
EVOLUTION OF INTEL x86 PROCESSORS

## Slide 6: CONTD…
Machine Evolution
  386 1985 0.3M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2000 42M
  Core 2 Duo 2006 291M
  Core i7 2008 731M
Added Features
  Instructions to support multimedia operations
  Instructions to enable more efficient conditional operations
  Transition from 32 bits to 64 bits
  More cores

## Slide 7: X86 Clones: Advanced micro devices (AMD)
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
Then
  Recruited top circuit designers from Digital Equipment Corp. and other downward trending companies
  Built Opteron: tough competitor to Pentium 4
  Developed x86-64, their own extension to 64 bits
Recent Years
  Intel got its act together
    Leads the world in semiconductor technology
  AMD has fallen behind
    Relies on external semiconductor manufacturer

## Slide 8: Layers and views of Computer System

## Slide 9: Computer System can be defined …
Simply put, a computer is a sophisticated electronic calculating machine that:
  Accepts input information,
  Processes the information according to a list of internally stored instructions and
  Produces the resulting output information.
Functions performed by a computer are:
  Accepting information to be processed as input.
  Storing a list of instructions to process the information.
  Processing the information according to the list of instructions.
  Providing the results of the processing as output.

## Slide 10: Evolution of Computer Systems
FIRST GENERATION (1945–1955)
• Program and data reside in the same memory (stored program concepts –John von Neumann)
• ALP was made used to write programs
• Vacuum tubes were used to implement the functions (ALU & CU design)
• Magnetic core and magnetic tape storage devices are used
• Using electronic vacuum tubes as the switching components

## Slide 11: Contd…
SECOND GENERATION (1955 – 1965)
• Transistor were used to design ALU & CU
• HLL is used (FORTRAN)
• To convert HLL to MLL compiler were used
• Separate I/O processor were developed to operate in parallel with CPU thus improving the performance
• Invention of the transistor which was faster smaller and required considerably less power to Operate

## Slide 12: Contd…
THIRD GENERATION (1965 ‐ 1975)
• IC technology improved
• Improved IC technology helped in designing low cost high speed processor and memory
modules
• Multiprogramming pipelining concepts were incorporated
• DOS allowed efficient and coordinate operation of computer system with multiple users
• Cache and virtual memory concepts were developed
• More than one circuit on a single silicon chip became available

## Slide 13: Contd…
FOURTH GENERATION (1975 ‐ 1985)
• CPU –Termed as microprocessor
• INTEL MOTOROLA TEXAS,NATIONAL semiconductors started developing
microprocessor
• Workstations, microprocessor (PC) & Notebook computers were developed
• Interconnection of different computer for better communication LAN,MAN,WAN
• Computational speed increased by 1000 times
• Specialized processors like Digital Signal Processor were also developed
BEYOND THE FOURTH GENERATION (1985 – TILL DATE)
E‐Commerce E‐banking, home office
• ARM, AMD, INTEL, MOTOROLA
• High speed processor‐ GHz speed
• Because of submicron IC technology lot of added features in small size

## Slide 14: Structure and Function of a Computer System
Structure: The way in which the components are interrelated.
Function: The operation of each individual component as part of the structure.

## Slide 15: Functions
The basic functions that a computer can perform. In general terms, there are only four:
• Data processing
• Data storage
• Data movement
• Control

## Slide 16: FUNCTIONAL VIEW OF THE COMPUTER SYSTEM

## Slide 17: Possible computer operations

## Slide 18: Contd…

## Slide 19: The Computer System – Top-level Structure

## Slide 20: References
W. Stallings, Computer Organization and Architecture, Design for Performance, 10th Edition, Prentice-Hall.