## Slide 1: UNIT 1
Organization of the von Neumann machine
Harvard architecture

## Slide 2: Designing Computers
All computers more or less based on the same basic design, the Von Neumann Architecture! – stored program concept

## Slide 3: The Von Neumann Architecture
Model for designing and building computers, based on the following three characteristics:
  The computer consists of four main sub-systems:
    Memory
    ALU (Arithmetic/Logic Unit)
    Control Unit
    Input/Output System (I/O)
  Program is stored in memory during execution.
  Program instructions are executed sequentially.

## Slide 4: The Von Neumann Architecture
Memory
Processor (CPU)
Input-Output
Control Unit
ALU
Store data and program
Execute program
Do arithmetic/logic operations requested by program
Communicate with
"outside world", e.g.
Screen
Keyboard
Storage devices
...
Bus

## Slide 5: Memory Subsystem
Memory, also called RAM (Random Access Memory),
  Consists of many memory cells (storage units) of a fixed size. Each cell has an address associated with it: 0, 1, …
  All accesses to memory are to a specified address. A cell is the minimum unit of access (fetch/store a complete cell).
  The time it takes to fetch/store a cell is the same for all cells.
When the computer is running, both
  Program
  Data (variables)
are stored in the memory.

## Slide 6: RAM
Need to distinguish between
  the address of a memory cell and the content of a memory cell
Memory width (W):
  How many bits is each memory cell, typically one byte (=8 bits)
Address width (N):
  How many bits used to represent each address, determines the maximum memory size = address space
  If address width is N-bits, then address space is 2N (0,1,...,2N-1)
...
0
1
2
2N-1
1 bit
W
0000000000000001
N
2N

## Slide 7: Memory Size / Speed
Typical memory in a personal computer (PC):
  64MB - 256MB
Memory sizes:
  Kilobyte (KB) = 210 = 1,024 bytes ~ 1 thousand
  Megabyte(MB) = 220 = 1,048,576 bytes ~ 1 million
  Gigabyte (GB) = 230 = 1,073,741,824 bytes ~ 1 billion
Memory Access Time (read from/ write to memory)
  50-75 nanoseconds (1 nsec. = 0.000000001 sec.)
RAM is
  volatile (can only store when power is on)
  relatively expensive

## Slide 9: Operations on Memory
Fetch (address):
  Fetch a copy of the content of memory cell with the specified address.
  Non-destructive, copies value in memory cell.
Store (address, value):
  Store the specified value into the memory cell specified by address.
  Destructive, overwrites the previous value of the memory cell.
The memory system is interfaced via:
  Memory Address Register (MAR)
  Memory Data Register (MDR)
  Fetch/Store signal

## Slide 10: Structure of the Memory Subsystem
Fetch(address)
  Load address into MAR.
  Decode the address in MAR.
  Copy the content of memory cell with specified address into MDR.
Store(address, value)
  Load the address into MAR.
  Load the value into MDR.
  Decode the address in MAR
  Copy the content of MDR into memory cell with the specified address.
MAR
MDR
...
Memory
decoder
circuit
Fetch/Store
controller
F/S

## Slide 11: Input/Output Subsystem
Handles devices that allow the computer system to:
  Communicate and interact with the outside world
    Screen, keyboard, printer, ...
  Store information (mass-storage)
    Hard-drives, floppies, CD, tapes, …
Mass-Storage Device Access Methods:
  Direct Access Storage Devices (DASDs)
    Hard-drives, floppy-disks, CD-ROMs, ...
  Sequential Access Storage Devices (SASDs)
    Tapes (for example, used as backup devices)

## Slide 12: I/O Controllers
Speed of I/O devices is slow compared to RAM
  RAM ~ 50 nsec.
  Hard-Drive ~ 10msec. = (10,000,000 nsec)
Solution:
  I/O Controller, a special purpose processor:
    Has a small memory buffer, and a control logic to control I/O device (e.g. move disk arm).
    Sends an interrupt signal to CPU when done read/write.
  Data transferred between RAM and memory buffer.
  Processor free to do something else while I/O controller reads/writes data from/to device into I/O buffer.

## Slide 13: Structure of the I/O Subsystem
I/O controller
I/O Buffer
Control/Logic
I/O device
Data from/to memory
Interrupt signal (to processor)

## Slide 14: The ALU Subsystem
The ALU (Arithmetic/Logic Unit) performs
  mathematical operations (+, -, x, /, …)
  logic operations (=, <, >, and, or, not, ...)
In today's computers integrated into the CPU
Consists of:
  Circuits to do the arithmetic/logic operations.
  Registers (fast storage units) to store intermediate computational results.
  Bus that connects the two.

## Slide 15: Structure of the ALU
Registers:
  Very fast local memory cells, that store operands of operations and intermediate results.
  CCR (condition code register), a special purpose register that stores the result of <, = , > operations
ALU circuitry:
  Contains an array of circuits to do mathematical/logic operations.
Bus:
  Data path interconnecting the registers to the ALU circuitry.
ALU circuitry
GT
EQ
LT
R0
R1
R2
Rn

## Slide 16: The Control Unit
Program is stored in memory
  as machine language instructions, in binary
The task of the control unit is to execute programs by repeatedly:
  Fetch from memory the next instruction to be executed.
  Decode it, that is, determine what is to be done.
  Execute it by issuing the appropriate signals to the ALU, memory, and I/O subsystems.
  Continues until the HALT instruction

## Slide 17: Structure of the Control Unit
PC (Program Counter):
  stores the address of next instruction to fetch
IR (Instruction Register):
  stores the instruction fetched from memory
Instruction Decoder:
  Decodes instruction and activates necessary circuitry
Instruction
Decoder
IR
+1
PC

## Slide 18
von Neumann
Architecture

## Slide 19: Harvard Architecture