## Slide 1: Instructions Formats

## Slide 2: IAS MACHINE
MEMORY: 4096 WORDS
WORD LENGTH: 40 BITS
STORED PROGRAM CONCEPT
DATA: SIGN BIT AND 39 BIT VAULE
TWO 20 BIT ISTRUCTIONS
EACH INSTRUCTION: 8 BIT OPCODE, 12 BIT ADDRESS (POINTS TO THE OPERAND IN THE MEMORY)

## Slide 3: IAS MEMORY FOMATS

## Slide 4
IAS Instruction set

## Slide 5
IAS Instruction set (continued)

## Slide 6: Problem
Write an appropriate assembly language code for the following operation and interpret to Von Neumann IAS architecture
X=Y*Z
// Where X->40 bit data and Y->40 bit data
Result would be more than 40 bit.

## Slide 7: EXAMPLE ALP (IAS)
Assume that data variables ‘Y’ & ‘Z’ available at memory locations 801 & 802 resly. And X will be stored 803 onwards.
LOAD MQ, M(801) MQM[801]
MUL M(802) AcMQ * M[802]
STOR M(803) M[803]AC
LOAD MQ ACMQ
STOR M(804) M[804]AC

## Slide 8: Fetch / Execute Cycle

## Slide 9
AC
MQ
Arithmetic & Logic Circuits
MBR
IBR
IR
Control
Circuits
PC
MAR
Input/output
Equipments
Main Memory
IAS Computer
MARPC
MBRM[MAR]
IRMBR<0..7>
MARMBR<8..19>
IBRMBR<20..39>
ACMBR
MBRM[MAR]
IRIBR<0..7>
MARIBR<8..19>
MBRM[MAR]
ACAC + MBR
PCPC+1
MARPC
MBRM[MAR]
IRMBR<0..7>
MARMBR<8..19>
IBRMBR<20..39>
M[MAR}MBR
MBRAC
IRIBR<0..7>

## Slide 10
AC
MQ
IBR
PC = 1
IR
MAR = 1
MEMORY
1. LOAD M(X) 500, ADD M(X) 501
2. STOR M(X) 500, (Other Ins)
.....
3
4
PC
MBR
IR
IBR
MAR
1
1
LOAD M(X) 500, ADD M(X) 501
AC
ADD M(X) 501
LOAD M(X)
500
3
ADD M(X)
501
2
4
2
STOR M(X) 500, (Other Ins)
(Other Ins)
STOR M(X)
500
3
7
MBR
Mar ← PC
add = 1
LOAD M(X) 500, ADD M(X) 501
ADD M(X) 501
LOAD M(X)
500
MAR =500
add = 500
MBR = 3
3
AC = 3
Add M(X)
501
MAR = 501
add = 501
PC = 2
4
MBR = 4
AC = 7
MAR ←PC
MAR = 2
add = 2
STOR M(X) 500, (Other Ins)
STOR M(X)
(Other Ins)
500
MAR = 500

## Slide 11
AC
MQ
IBR
PC = 1
IR
MAR = 1
MEMORY
1. LOAD M(X) 500, ADD M(X) 501
2. STOR M(X) 500, (Other Ins)
.....
3
4
PC
MBR
IR
IBR
MAR
1
1
LOAD M(X) 500, ADD M(X) 501
AC
ADD M(X) 501
LOAD M(X)
500
3
ADD M(X)
501
2
4
2
STOR M(X) 500, (Other Ins)
(Other Ins)
STOR M(X)
500
3
7
MBR
Mar ← PC
add = 1
LOAD M(X) 500, ADD M(X) 501
ADD M(X) 501
LOAD M(X)
500
MAR =500
add = 500
MBR = 3
3
AC = 3
Add M(X)
501
MAR = 501
add = 501
PC = 2
4
MBR = 4
AC = 7
MAR ←PC
MAR = 2
add = 2
STOR M(X) 500, (Other Ins)
STOR M(X)
(Other Ins)
500
MAR = 500

## Slide 12: Example Problems
Write an Assembly language programming for the following expressions using IAS computer Instruction set and interpret to the flow of IAS computer
  1. A=(B-C)*D
  2. A=B*(C+D)
Make necessary assumptions.

## Slide 13
Computer Components: Top Level View

## Slide 14
Instruction Cycle
The IAS operates repetitively performing an instruction cycle.
Each instruction cycle consists of Two subcycles.
Two steps:
  Fetch
  Execute

## Slide 15
Fetch Cycle
Program Counter (PC) holds address of next instruction to fetch
Processor fetches instruction from memory location pointed to by PC
Increment PC
  Unless told otherwise
Instruction loaded into Instruction Register (IR)
Processor interprets instruction and performs required actions

## Slide 16
Execute Cycle
Processor-memory
  data transfer between CPU and main memory
Processor- I/O
  Data transfer between CPU and I/O module
Data processing
  Some arithmetic or logical operation on data
Control
  Alteration of sequence of operations
  e.g. jump
Combination of above

## Slide 18
Instruction Cycle State Diagram

## Slide 19: Instruction state cycle diagram (cont..)
Instruction address calculation (iac):
  Determine the address of the next instruction to be executed. Adding a fixed number to a next number.
Instruction fetch: (if)
  Read the instruction from its memory location into the processor.
Instruction operation decoding (iod)
  Analyze instruction to determine type of operation to be performed and operand(s) to be used.
Operand Address Calculation: (oac)
  If the operation involves the reference to an operand in memory or available via I/O, then determine the address of the operand.
Operand Fetch (of):
  Fetch the operand from memory or read it from I/O.
Data Operation (do):
  Perform the operation indicated in the instruction.
Operand store (os)
  Write the result into memory or out to I/O.

## Slide 20
Characteristics of Hypothetical Machine

## Slide 21: Characteristics of Hypothetical Machine (cont..)
The processor contains a single data register called an accumulator (AC). Both instructions and data are 16 bits long. Thus it is convenient to organize memory using 16 bit words.
The instruction format provides 4 bits for the opcode, so that there can be as many as 24 =16 different opcodes, and upto 212= 4096(4K) words of memory can be directly addressed.

## Slide 22
Example of Program Execution

## Slide 23: Instruction
Definition:
  Instruction is a statement by which the operation of CPU is determined.
  These instructions referred as “Machine instructions or computer Instructions”
  The collection of different instructions that the CPU can execute is referred to as the CPU’s instruction set.

## Slide 24
What must an instruction set specify…?

## Slide 25
Which Operation to perform
Where to find the operand or operands
Where to put the result, if there is result
Where to find the next instruction

## Slide 26: Instruction Representations
Each instruction is represented by sequence of bits
The instruction is divided into two fields
  Opcode field
  Operand field
This operand field further divided into one to four fields.
This layout of the instruction is known as the “Instruction Format”
Simple instruction format
Opcode
Operand
Address1
Operand
Address2
Result
Address1
Next
Instruction

## Slide 27: CLASSIFICATION OF INSTRUCTIONS